FORM - V

(See rule 14)

Environmental Statement (form-v) report

for the financial Year ending 31st March, 2019.

# PART – A

i) Name and address of the owner/	:	Mr. N. PURUSHOTHAMA RAO

occupier of the industry operation                                    Managing Director,

or process.					M/s. PORUS LABORATORIES PVT. LTD.,

UNIT-VI,

Plot No:2A, APSEZ, Moturupalem (V), Atchutapuram, Rambilli (M),

Visakhapatnam-531011, Andhra Pradesh

ii) Date of the last environmental	:	First Time

audit report submitted

iii) Production Capacity (Units)	      	:

iv) Year of Establishment		:

| Sl. No |  | Production Quantity (Kg/Day) |
| --- | --- | --- |
| 1. | p-Phenolphthalein bisphenol (or) 2-Phenyl-3,3-bis (4-hydroxy phenyl) phthalimide (PPPBP) | 7666.7 |
| 2. | 4-Nitro-N-methyl phthalimide (4-NPI) | 13333.3 |
| 3. | 1,3-Cyclohexadiene | 33.3 |
| 4. | Cupreidine | 16.7 |
| 5. | 2-(1-Chlorocyclopropyl)-2-[(2-chlorophenyl) methyl]-oxirane | 666.7 |
| 6. | Polyterpene | 33.3 |
| 7. | Sulfonated Polymer | 333.3 |
| 8. | Un-Hydogenated Styrenic Block Copolymer (USBC) | 333.3 |
| 9. | Hydogenated Styrenic Block Copolymer (HSBC) | 333.3 |
| 10. | TOFA Plasticizer | 333.3 |
| 11. | R&D Products | 10.0 |
| Grand Total (Total Products) | 23,093.20 |

PART – B

# WATER AND RAW MATERIAL CONSUMPTION

i) Water consumption (Kl/day):  603.9

| 1 | Process | 366.9 |
| --- | --- | --- |
| 2 | Washings | 20.0 |
| 3 | Boiler | 100.0 |
| 4 | Cooling Towers make-up | 50.0 |
| 5 | DM Plant regeneration | 10.0 |
| 6 | Softener Plant Regeneration | 10.0 |
| 7 | R&D, Q.C | 5.0 |
| 8 | Scrubber | 12.0 |
| 9 | Domestic | 10.0 |
| 10 | Gardening | 20.0 |

------------------------------------------------------------------------------------------------------------------------------Name of Products    		 Water consumption per unit of products (L/Kg)

--------------------------------------------------------------------------------

During the previous	During the current

financial year        		financial year

(2017-2018)               	(2018-2019)

------------------------------------------------------------------------------------------------------------------------------

1. P-Phenolphthalein bisphenol (or)

2-Phenyl-3,3-Bis (4-Hydroxy Phenyl)

Phthalimide (PPPBP)				Nil			14.210

-----------------------------------------------------------------------------------------------------------------------------

ii) Raw material consumption:

------------------------------------------------------------------------------------------------------------------------------

Name of raw       		Name of        	  Consumption of raw material

materials         		product

-----------------------------------------------------------------------

During the previous	During the current

financial year 		financial year

(2017-2018)          	 (2018-2019)

------------------------------------------------------------------------------------------------------------------------------

P-Phenolphthalein bisphenol (or)2-Phenyl-3,3-Bis (4-Hydroxy Phenyl) Phthalimide (PPPBP)

- Phenolphthalein                                   Nil                        0.947

- Aniline					Nil			0.0.32

- HCL						Nil			2.320

- CS Lye					Nil			1.815

- Methanol                                           Nil                         0.400

----------------------------------------------------------------------------------------------------------------------------

PART - C

# POLLUTION DISCHARGED TO ENVIRONMENT

(Parameter’s as specified in the consent issued)

| Pollutants | Quantity of Pollutants Discharged (kg/day) 2018-2019 | Concentrations Of Pollutants in Discharges (mg/L) 2018-2019 | Percentage of variation from prescribed standards of APPCB for CETP |
| --- | --- | --- | --- |
| a) wastewater: | The industry shall segregate the HTDS and LTDS effluent streams and the effluents after neutralisation HTDS & LTDS shall be sent to CETP of Pharmacity for further treatment. |

| b) Air |
| --- |
| Stack Attached to | Pollutants | Quantity of Pollutants in Emissions (kg/day) 2018-2019 | Concentrations Of Pollutants in Emissions (mg/nm3) 2018-2019 | APPCB Prescribed Limits | Percentage of variation from prescribed standards with reasons |
| Coal Fired Boiler 10TPH | SPM | 19.85 | 85 | 115 | 26.08 % Less |
|  | SO2 | 39.47 | 169 | 800 | 78.87 % Less |
|  | NOx | 17.05 | 73 | 600 | 87.83 % Less |
| 500 KVA D.G. Set | SPM | 1.68 | 64 | 115 | 44.34 % Less |
|  | SO2 | 3.32 | 126 | 800 | 84.25 % Less |
|  | NOx | 5.67 | 215 | 600 | 64.16 % Less |
| 1000 KVA D.G. Set - I | SPM | 2.48 | 65 | 115 | 43.47 % Less |
|  | SO2 | 6.18 | 162 | 800 | 79.75 % Less |
|  | NOx | 9.04 | 237 | 600 | 60.50 % Less |
| 1000 KVA D.G. Set - II | SPM | 2.67 | 69 | 115 | 40.00 % Less |
|  | SO2 | 6.11 | 158 | 800 | 80.25 % Less |
|  | NOx | 9.91 | 256 | 600 | 57.33 % Less |

#### PART – D

HAZARDOUS WASTE

(As specified under Hazardous and other wastes Management and Transboundary Movement Rules, 2016)

------------------------------------------------------------------------------------------------------------------------------

Hazardous Wastes                			Total Quantity per year

-------------------------------------------------------------------------------

During the previous  		During the current

financial year        		financial year

(2017-2018)             	          (2018-2019)

----------------------------------------------------------------------------------------------------------------------------

i)   Waste oil					  Nil		                          Nil

ii) Detoxified containers

a) HDPE drums		           Nil		                         100

b) Plastic bags			 Nil		                       1.500

c) Carboys			           Nil	                                    50

------------------------------------------------------------------------------------------------------------------------------

PART - E

SOLID WASTES

-----------------------------------------------------------------------------------------------------------------------------

Total Quantity per year

----------------------------------------------------------------------

During the previous  	During the current

financial year        		financial year

(2017-2018)              	(2018-2019)

------------------------------------------------------------------------------------------------------------------------------

1)	Organic residue (MT)			Nil			27.710 MT

2)	ETP sludge (MT)				Nil			Nil

3)	Spent carbon (MT)				Nil			44.640 MT

4)	Coal Ash (Units)- MT		          Nil			540.00 MT

------------------------------------------------------------------------------------------------------------------------------

PART - F

Please specify the characteristics (in terms of concentration and quantum) of Hazardous as well as solid wastes and indicates disposal practice adopted for both these categories of wastes.

Solid waste generation in the plant i.e Distillation residue, spent carbon is being sent to Cement Industries. Used oil and detoxified drums and etc. are sold to authorized agencies of A.P.P.C.B.

PART – G

Impact of the pollution control measures on conservation of natural resources and consequently on the cost of production.

Adequate measures taken to maintain clear environment in and around the factory premises. There is a bare minimum impact on the surrounding environment.

PART - H

Additional investment proposal for environmental protection including abatement of pollution.

Company has spent around Rs. 120.0 Lakhs (Rupees One hundred and twenty lakhs only) per year on pollution control facilities for the financial year 2018-2019. i.e. operation and maintenance of ETP.

PART - I

Any other particulars in respect of environment protection and abatement of pollution.

The green belt is developed, steps taken by the management to abate pollution and at the same time improves the surrounding environment.

AUDITOR’S COMMENTS:

- Under A.P.P.C.B clean & green programme M/s. PORUS LABORATORIES PVT.LTD., (UNIT-VI) is maintaining greenbelt with total 10,000 No’s plants have been planted in this financial year 2018-2019.

- The company has spent Rs. 120.0 Lakhs (Rupees One hundred twenty lakhs only) during the financial year 2018-2019 for Operation & Maintenance of pollution control facilities.

Auditor’s Signature